### Git Repositories:
ros-node-devel: currently up-to-date
zahedim/pcb-development: hardware revision #1
chris_work_stable: pid control for motors, read odometry data, Teensy++ 2.0 DK

### Folder structure:
+ datasheets:
+ amp: LM324-N, low-power, quad-operational amplifier used in robofriends head
+ servo: SD20, 20 channel I²C servo controller used in robofriends head
+ uc: data sheet, info, schematics and pin out information for Teensy++ 2.0 DK
+ usb: CY7C63743C, USB controller used in robofriends head
+ documentation:
+ WS17: master thesis Karima Khlousy-Neirukh
+ WS18: battery value percentage mapping, hardware overview, robofriend overview
+ pcb:
+ bom: last updated on 17th of May 2019
+ gerber: last generated on 17th of May 2019
+ img: FH Technikum Wien Logo
+ kicad: KiCad project files
+ lib: needed libraries and footprints for KiCad
+ plot: schematics plotted
+ track-width: track widths used for pcb layout
+ simulation:
+ supply: ltspice simulation files used for power supply pcb
+ vbat: ltspice simulation files used for the voltage divider measuring the battery voltage
+ src:
+ Pi: code used for raspberry pi
+ TabletGUI: code used for TabletGUI
+ Teensy: code used for Teensy++ 2.0 DK

### Schmeatics info:
- Input Filter and Power Plugs:
  - Connect up to three parallel 12 V batteries to J2
  - Deep discharge protection:
    - The hysteresis width is designed for 1 V
    - Used formula (see this link):
      UTP = (R3 / (R3 + R5)) * +VCC = (20 k / (20 k + 220 k)) * 12 V= 1 V
      LTP = (R3 / (R3 + R5)) * -VCC = (20 k / (20 k + 220 k)) * 0 V= 0 V
      VHYS = UTP - LTP = 1 V
    - Use RV1 to adjust the VREF (see the simulation files)
  - 12 V supply for robofriend’s peripheral:
    - Solder J16 if you are not using a buck boost converter, otherwise
    - Use J11 as an unregulated 12 V output for a buck boost converter
    - Connect the regulated 12 V supply to J20
  - Power up an additional raspberry pi via J13 or J14
- Overcurrent Detection/Protection
  - D8 signals that the boost modules are supplied with 12 V
  - INA193 is a current shunt monitor with an analog linear output presenting 10 A of current consumption as 2 V at its output (link).
  - Current consumption by a single motor:
    - no-load: 0.18 A
    - rated: 0.35 A
    - max.: 3.50 A
  - The analog output signal is used as an input for a comparator (U9) to generate a digital signal which can be registered as an external interrupt
  - Use RV2 to adjust VREF (see the simulation files)
- Precision shunt VREF
  - 4.096 V precision shunt used as VREF for ADC measurements (connect JP4)
- Teensy++ 2.0:
  - Connect JP1 when the development kit is placed on the pcb socket
  - Disconnect JP1 when just using the USB interface to power up the development kit
- General:
  - Check the logic level before connecting external peripheral to the pcb

### Repository Setup/ROS Installation/Setup/Configuration info:
Link for the project setup.
### Robofriend - General info:
Link.